## Slide 1
Introduction to Point Clouds

## Slide 2: What is Point Cloud Data (.pcd)?
A point cloud is just a bunch of tiny 3D points that together form the shape of a real object or environment.
Each point has:
x → left-right
y → forward-backward
z → up-down
Each point shows where something is in 3D space.
No lines or surfaces — just a cloud of dots that shape an object or scene.
It’s like a 3D version of a connect-the-dots image, but without the lines.
Point clouds can also contain extra data:
Color (RGB)
Intensity (how strong the laser reflection was)
Labels (if annotated)
Used to recreate, analyze, or understand the physical world digitally.

## Slide 3: Point Cloud Data

## Slide 5: 1. LiDAR (Light Detection and Ranging)
  Sends laser beams.
  Measures time taken for light to return.
  Calculates distance for each point.
  Builds a 3D view of the surroundings.
  Common in: Self-driving cars, robots, drones.

## Slide 6: Stereo Cameras
  Has two lenses, like our eyes.
  Takes two pictures from slightly different angles.
  Calculates depth by comparing differences between the two.
  Example: Human eye depth perception.
  Used in: Robotics, drones, stereo vision systems.

## Slide 7: Depth Cameras
    Captures how far each pixel is from the camera.
    Types:
    Stereo Depth Camera – like above.
    Structured Light Camera – projects a grid/pattern, sees how it bends.
    Time of Flight (ToF) – sends light, measures bounce-back time.
    Output: Depth Map (white = close, black = far)
    Used in: Face ID, AR/VR, 3D scanning.

## Slide 8: Real-World Applications of Point Clouds
  A. Robotics
  Robots use point clouds to:
  Detect and avoid obstacles
  Pick and place objects
  Navigate in 3D space
  B. ADAS (Advanced Driver Assistance Systems)
  Cars use LiDAR & cameras to:
  Detect vehicles, pedestrians, lanes
  Help with braking, parking, and lane-keeping
  Power self-driving technology
  C. 3D Mapping & Scanning
  Architects and surveyors scan buildings/land
  3D point clouds help create accurate digital models

## Slide 9
PCD File Format Basics

## Slide 10: .PCD File?
.pcd = Point Cloud Data file format.
It stores 3D points in a special format.
Each file has:
A header (information about the data)
A list of points (x, y, z, and sometimes rgb)

## Slide 11: Fields in a .PCD File
(Example: x y z rgb)
x: left-right position
y: up-down position
z: forward-backward position
rgb: color of the point
Think of each point like:
(where it is) + (what color it is)

## Slide 12: Fields in a .PCD File
If DATA ascii is used, you can open it in Notepad/VS CODE/Text editor
Each line = one point
Example: 25.2 -19.5 15.4
A 3D point at that position
You can add/edit points by changing numbers (carefully!)

## Slide 13: Manually Editing a .PCD File
If DATA ascii is used, you can open it in Notepad/VS CODE/Text editor
Each line = one point
Example: 25.2 -19.5 15.4
A 3D point at that position
You can add/edit points by changing numbers (carefully!)

## Slide 14: ASCII vs BINARY in .PCD Files
Use ASCII for learning, Binary for performance

## Slide 15: Common Header Errors (and Fixes)
Error: POINTS doesn't match the number of lines
Fix: Count lines and update the POINTS value
Error: Wrong FIELDS (e.g., missing rgb)
Fix: Add correct fields based on your data
Error: File says binary but it’s text
Fix: Change DATA ascii or re-save correctly

## Slide 16: ASCII Point Example
If header says FIELDS x y z, then each line looks like:
12.5 10.0 3.4
If header says FIELDS x y z rgb, then:
12.5 10.0 3.4 5.62034e-33

## Slide 17: What is ASCII?
ASCII = American Standard Code for Information Interchange
It's how computers save text using numbers
In .pcd, ASCII format means:
You can read/edit the points
But it takes more space than binary

## Slide 18: Comparing Two Example Files

## Slide 19
PCD File Deep Dive

## Slide 20: What Are Point Attributes?
Attributes = Extra details stored for each point
Each tiny dot in the image (like the yellow machine, soil, trees) is a 3D point with attributes
In Image each point has:

## Slide 21: Loading Point Cloud in Python (Open3D)
Install Open3D - pip install open3d
Load and view file :
import open3d as o3d
Read - pcd = o3d.io.read_point_cloud("image_0002.pcd")
Visualize - o3d.visualization.draw_geometries([pcd])
Save - o3d.io.write_point_cloud("copy.pcd", pcd)

## Slide 22: What Does FIELDS x y z rgb Mean?
In .pcd files, FIELDS tells us what each point contains
Example from our file:
FIELDS x y z rgb
This means each point has:
x – left/right position
y – up/down position
z – depth (forward/backward)
rgb – color of the point
Each point = Position + Color

## Slide 23: What is Version?
Our file has: VERSION 0.7
This tells the format version of the file
Version 0.7 is commonly used and supported by most tools
No action needed

## Slide 24: What is Endianess?
Endianess = how computers store bytes
It only matters in binary files
Our file uses:
DATA ascii - it’s human-readable and editable!

## Slide 25
Point Cloud Data Exploration

## Slide 26: Objectives :
Inspecting point attributes
Visualizing point clouds in Open3D
Basic statistics (min, max, mean)
Scaling
Normalization
Standardization
Outlier detection
Visualization techniques

## Slide 27: Inspecting Point Attributes
Each point can include:
x = 1.5, y = -2.0, z = 3.0, rgb = 3.4e-38
Use .fields in PCD headers or np.asarray(pcd.points) in Open3D

## Slide 28: Visualizing Point Clouds in Open3D
import open3d as o3d pcd = o3d.io.read_point_cloud("yourfile.pcd") o3d.visualization.draw_geometries([pcd])
Lets you:
Rotate and zoom the cloud
Visually inspect shape, density, and color
Check noise or misalignment

## Slide 29: Basic Statistics – Min, Max, Mean
Used to understand:
The size of the cloud
The center point
How spread out the data is
Formulas :
min_coords = points.min(axis=0)
max_coords = points.max(axis=0)
mean_coords = points.mean(axis=0)
What you get:
min_x, min_y, min_z → Smallest values
max_x, max_y, max_z → Largest values
mean_x, mean_y, mean_z → Average (center)

## Slide 30: Scaling (Min-Max Scaling)
Purpose: Resize the point cloud into a fixed range (e.g., 0 to 1)
Formula: X_scaled = (X - X_min) / (X_max - X_min)
Do this for X, Y, and Z separately
Use for:
Matching display space
Input to ML models
Removing unit mismatches (cm vs m)

## Slide 31: Normalization
Purpose:
Move the point cloud to the center and scale to standard size
1.Centering: X_centered = X – mean
2. Scaling: X_normalized = X_centered / max(|X_centered|)
Result:
Cloud is centered at (0,0,0)
Fits within a unit cube (-1 to 1)
Used before ML training or aligning clouds

## Slide 32: Scaling and Normalization
Scaling just changes the size — like zooming in or out. Normalization shifts the point cloud to the center and resizes it to fit within a box from -1 to 1, so it’s easier to compare with other clouds.”
The chair has now
been centered at the origin (0, 0, 0)
resized to fit within a unit cube
from -1 to +1 on all axes

## Slide 33: Standardization
Transforms point cloud data so:
Mean = 0
Standard deviation = 1
Makes all axes centered and equally scaled
Formula: (X_standardized = (X - μ) / σ)
standardized_value = (value - mean) / std_dev
Apply to x, y, z individually
Used for machine learning and statistical analysis

## Slide 34: Outlier Detection (Noise Removal)
What are Outliers?
Points far from the main structure of the cloud
Usually caused by noise, reflections, or sensor errors
Checks how far each point is from its neighbors
Removes those that are too isolated

## Slide 35: Visualization Techniques
Tools:
Open3D
CloudCompare
MeshLab
PCL Viewer
What You Can View:
Color by height or intensity
Bounding boxes / coordinate axes
Normals (surface directions)
Before/After filtering comparison
Always visualize before and after processing

## Slide 36
Working with Point Cloud Tools

## Slide 37: Objectives :
Understand key tools used for point cloud data
Learn to install and set up tools
Perform basic processing like noise removal and downsampling

## Slide 38: Tool Overview – Open3D, PCL, and ROS RViz
Open3D
Python-based library
Used for point cloud loading, visualization, filtering, etc.
Very beginner-friendly
PCL (Point Cloud Library)
C++ library for advanced point cloud processing
Supports segmentation, filtering, alignment, etc.
Requires some programming setup
ROS RViz
Part of ROS (Robot Operating System)
Real-time 3D visualization tool
Great for viewing LiDAR and robot data in robotics

## Slide 39: Installing Open3D
Steps to Install Open3D (Python):
pip install open3d
Works on Windows, Linux, Mac
Best for beginners with Python knowledge
You can use Jupyter Notebook or plain Python scripts

## Slide 40: Installing PCL – C++ Library
Available via system packages (Linux):
sudo apt install libpcl-dev
Requires:
C++ compiler (GCC)
CMake for building
Advanced use; best for robotics and performance-critical applications

## Slide 41: ROS RViz Setup
Install ROS (e.g., Noetic) on Ubuntu:
sudo apt install ros-noetic-desktop-full
Comes with RViz pre-installed
Best for roboticists visualizing sensor data like LiDAR

## Slide 42: Load and View Point Cloud in Open3D
Python Example:
import open3d as o3d
pcd = o3d.io.read_point_cloud("yourfile.pcd")
o3d.visualization.draw_geometries([pcd])
This opens a 3D viewer window
You can rotate, zoom, and explore the point cloud

## Slide 43: Remove Noise – Clean the Data
Why?
Point clouds often have random isolated points → not useful
Use Statistical Outlier Removal:
clean_pcd, ind = pcd.remove_statistical_outlier(nb_neighbors=20, std_ratio=2.0)
o3d.visualization.draw_geometries([clean_pcd])
Removes noisy, scattered points
Makes your data cleaner and easier to work with

## Slide 44
Why?
Too many points = slow processing
We only need enough to represent the shape
How it works:
Break 3D space into small cubes (voxels)
Keep 1 point per cube, remove extras
down_pcd = pcd.voxel_down_sample(voxel_size=0.05)
o3d.visualization.draw_geometries([down_pcd])
Faster processing
Smaller file size
Still preserves shape

## Slide 45: Save the Processed Cloud
o3d.io.write_point_cloud("cleaned_output.pcd", down_pcd)
Save your filtered or downsampled cloud to use later
Can be opened again in Open3D or other tools

## Slide 46
Point Cloud Preprocessing Concepts

## Slide 47: Objectives :
Customize PointCloud Visualization (Color, Size, Background)
Use RViz with ROS
Play PointClouds using a ROS Bag File
Live Demo + Hands-On Practice

## Slide 48: What is a .bag File?
.bag = "ROS bag file" — like a black box recorder for robots
Stores sensor data, TF, images, GPS, LiDAR, etc.
Used for playback and offline debugging
Plays back data as if the robot is alive again

## Slide 49: Playing a ROS Bag File
Open a terminal
Run: rosbag play -l <your_file.bag>
-l means loop continuously
Topics get published as if the robot is alive again

## Slide 50: Launching RViz
To start RViz: run rviz in a terminal
Left panel → “Displays”
Top area → “Global Options” for Fixed Frame and Background

## Slide 51: Add PointCloud2 Display in RViz
Click “Add” → Choose PointCloud2
Set Topic: /Lidar1PointCloud (or other topic)
Set Fixed Frame: map (or base_link if applicable)
Adjust view → You should see the cloud

## Slide 52: Customize – PointCloud Visualization
In PointCloud2 settings:
Color Transformer: RGB / Intensity / FlatColor
Size (m): 0.03 to 0.1
Style: Points
Alpha: 1.0 (fully visible)

## Slide 53: Customize – RViz Background
Go to “Global Options”
Change Background Color
Use Light Gray / Black for better contrast

## Slide 54: Multiple PointClouds
Add multiple PointCloud2 displays
Set topics: /Lidar1PointCloud, /Lidar2PointCloud, etc.
Publish static transforms for each one
Example :

## Slide 55: Recap & Key Takeaways
RViz is essential for debugging & visualization
Color and size customization improves clarity
Always check:
Topic name
Frame ID
Static TF link to map or base_link
Use .bag playback for safe offline testing

## Slide 56
Visualization Deep Dive (RViz + ROS)

## Slide 57: What is Point Cloud Preprocessing?
Few Points :
Preprocessing = cleaning and preparing raw 3D point data
Makes the cloud usable for analysis, visualization, or machine learning
We use it on our sample file: 1398110231.025_ascii.pcd

## Slide 58: Step 1 – Cleaning (Removing NaNs and Noise)
Raw point clouds can contain NaNs or invalid values
These points do not represent real objects
Removing them improves stability and quality
In Python with Open3D:
pcd.remove_non_finite_points()

## Slide 59: Step 2 – Outlier Removal
Some points may be isolated or flying in space
They don’t belong to surfaces (like walls or objects)
2 Common Methods:
Statistical Outlier Removal
Radius Outlier Removal
pcd, ind = pcd.remove_statistical_outlier(nb_neighbors=20, std_ratio=2.0)

## Slide 60: Step 3 – Centering
The point cloud may be located far from the origin
Centering moves the cloud so its "middle" is at (0,0,0)
This helps with visualization and alignment
Example:
center = np.mean(np.asarray(pcd.points), axis=0) pcd.translate(-center)

## Slide 61: Step 4 – Normalizing
Normalizing scales the cloud into a standard size (unit sphere or cube)
Useful for machine learning, comparison, or visualization
Makes different clouds consistent in size
Example:
points = np.asarray(pcd.points)
scale = np.max(np.linalg.norm(points, axis=1))
points /= scale
pcd.points = o3d.utility.Vector3dVector(points)

## Slide 62: How it Works ?
Sample Visualization

## Slide 63: Summary of Preprocessing Steps
Tool used: Open3D (Python)
Step | Purpose
Cleaning | Remove NaNs or invalid points
Outlier Removal | Remove noise and stray points
Centering | Move cloud to origin (0,0,0)
Normalizing | Scale cloud to fit within a unit boundary

## Slide 64
Filtering Methods

## Slide 65: Objectives :
filtering Methods
Radius Outlier filtering
statistical filtering
Visualization Befor/After filtering

## Slide 66: Introduction to Point Cloud Filtering
Point clouds often contain outliers (stray/noisy points)
These can come from:
Reflections
Sensor glitches
Wrong depth readings
Goal: Remove unwanted points while keeping shape intact

## Slide 67: Why Is Filtering Important?
Removes stray “flying” points
Improves processing speed
Boosts accuracy for:
SLAM
Object detection
3D reconstruction
Helps make point cloud clean, compact, and usable

## Slide 68: Types of Filtering Techniques
You will learn:
Radius Outlier Filtering
Statistical Outlier Filtering
And how to visualize the difference

## Slide 69: Radius Outlier Filtering – Concept
Checks:
“How many nearby points are within a fixed radius?”
If a point has fewer neighbors than threshold, it's removed
Simple but may miss dense outliers
Radius Outlier Filtering – How It Works ?
Parameters:
nb_points: Minimum number of neighbors
radius: Distance to check
Example :
Only keeps points with ≥5 neighbors within 10cm
pcd, ind = pcd.remove_radius_outlier(nb_points=5, radius=0.1)

## Slide 70: Radius Filtering – Real-World Analogy
Example:
Imagine 50 people in a room. For every person, we draw a circle around them. If they have less than 5 people inside that circle, we remove them. That’s how radius filtering works.

## Slide 71: Statistical Outlier Filtering
Looks at distance to neighbors
If a point is too far away from the average, it's removed
Uses standard deviation for thresholding
Smarter and more consistent

## Slide 72: Statistical Filtering – How It Works
Parameters:
nb_neighbors: Number of nearest points to use
std_ratio: Acceptable deviation from average
Example:
Keeps points that fall within 2 standard deviations from mean distance
pcd, ind = pcd.remove_statistical_outlier(nb_neighbors=20, std_ratio=2.0)

## Slide 73: Statistical Filtering – Real-World Analogy
Imagine:
If most people in a group stand 1 meter apart, and one person is 10 meters away, they're not really part of the group. So we remove them.

## Slide 74: Before & After Visualization
Step | Output
Original cloud | Noisy cloud with outliers
After Radius Filter | Fewer floating points, but some remain
After Statistical | Cleaner cloud with tight surface grouping

## Slide 75: Python :
o3d.visualization.draw_geometries([pcd]) # original
pcd_radius, _ = pcd.remove_radius_outlier(5, 0.1)
o3d.visualization.draw_geometries([pcd_radius])
pcd_stat, _ = pcd.remove_statistical_outlier(20, 2.0)
o3d.visualization.draw_geometries([pcd_stat])

## Slide 76: Which One Should I Use?
Situation | Best Filter
You want fast, simple cleanup | Radius Outlier
You want better accuracy | Statistical Filter
Working on small local cloud | Radius Outlier
Cleaning large scene globally | Statistical Filter

## Slide 77
voxelization & DownSampling

## Slide 78: Day - 10
why downsample?
voxel grid filters
Uniform Downsampling

## Slide 79: What is Voxel Grid Filtering?
Voxel Grid Filtering is a method of downsampling a point cloud by dividing the 3D space into small cubes (called voxels) and replacing all points inside each voxel with one point — usually the average (centroid) of the points.

## Slide 80: Key Idea:
Instead of storing all the original points, you:
Cut the space into a grid of small cubes
In each cube (voxel), you keep just one point
That one point represents all the others in that cube

## Slide 81: Why Use It?
Purpose | Benefit
Reduce data size | Faster computation & less memory
Remove redundancy | Nearby points get merged
Speed up processing | Ideal for SLAM, mesh, ML pipelines
Uniform sampling | Helps create structured clouds

## Slide 82: How It Works :
Choose a voxel size (e.g., 0.05 meters)
Break the 3D space into a grid of cubes
For each cube:
  Check how many points fall inside
  Compute the average position (x, y, z)
  Keep only 1 point
Discard the rest

## Slide 83: Example in Python (Open3D):
import open3d as o3d
pcd = o3d.io.read_point_cloud("sample.pcd")
voxel_down = pcd.voxel_down_sample(voxel_size=0.05)
o3d.visualization.draw_geometries([voxel_down])

## Slide 84: What Does Voxel Size Mean?
It defines the size of each 3D cube (voxel) used to group points.
Example:
voxel_size = 0.05 → Each voxel is a cube of 5 cm × 5 cm × 5 cm
voxel_size = 0.10 → Each voxel is 10 cm per side
The smaller the voxel size, the more detail you preserve. The larger the voxel size, the more aggressive the downsampling.

## Slide 85: How to Choose the Voxel Size?
Situation | Recommended Voxel Size
LiDAR car data (large scenes) | 0.1 to 0.5 meters
Indoor mapping | 0.02 to 0.1 meters
3D object models / meshes | 0.005 to 0.05 meters
Fast processing with rough shape | 0.1+ meters
High precision for ML/meshing | 0.01–0.02 meters

## Slide 86: Which term should you use?
Open3D (Python)
voxel_down_sample()
PCL (C++)
VoxelGrid filter class
Point cloud papers
"voxelization" or "voxelized cloud"

## Slide 87: Two common methods:
Voxel Grid Downsampling
Uniform Downsampling

## Slide 88: Why Downsample?
Large point clouds are slow and heavy
Many points are redundant (very close together)
Downsampling keeps the overall shape, but reduces size
Helps in:
  Visualization
  Mesh reconstruction
  Machine learning & segmentation

## Slide 89: What is Uniform Downsampling?
Keeps every Nth point in the point cloud (e.g., every 5th point)
Based on index, not spatial location
Very fast, but may lose important structure
Best for previews or debugging
Example:
pcd.uniform_down_sample(every_k_points=5)

## Slide 90: When Uniform Downsampling IS Useful ?
Situation | Why it's useful
You want to quickly reduce point count | Super fast and easy
Doing a quick test or preview | You just need a rough cloud
Debugging or prototyping code | You don’t need full detail
Working with structured point clouds (like grids or ordered scans) | Downsampling stays relatively balanced

## Slide 91: When It's Not Recommended ?
Uniform Down Sampling :
Situation | Why it’s risky
You need to preserve 3D structure | It removes points blindly
Feeding into ML or feature extraction | You might lose important features
Doing meshing, registration, or surface fitting | Missing points can cause artifacts

## Slide 92: Voxel vs Uniform Downsampling
Feature | Voxel Grid | Uniform Downsampling
Based on position? | Yes | No (based on index)
Preserves structure? | Mostly | Risk of random loss
Speed | Fast | Very fast
Use case | Accurate simplification | Rough preview/debugging

## Slide 93: When to Use Each ?
Use voxel grid filtering when:
  You need structure-preserving simplification
  Preparing data for ML, meshing, registration
Use uniform downsampling when:
  You want a quick, light version of the cloud
  Previewing or testing a pipeline

## Slide 94
Estimating Normals

## Slide 95: Estimating Normals in Point Clouds
Normals describe the surface direction at each point in a point cloud
They are essential for surface reconstruction, shading, and understanding object orientation
In this session, we’ll cover:
What normals are
How they’re estimated
KNN vs Radius neighborhood methods
Visualization techniques

## Slide 96: What Are Normals?
A normal is a small arrow that points perpendicular to the surface at a point
Every point in a cloud can have its own normal
Think of it like grass blades growing out of the surface
Why Normals Matter:
For shading and rendering
For surface/mesh reconstruction
For robot perception and pose estimation
For understanding surface geometry

## Slide 97: How Are Normals Estimated?
We don’t have surfaces — just points — so we guess normals using nearby points
Estimation Process:
Pick a point
Find its neighboring points
Fit a small plane through those neighbors
The vector perpendicular to that plane = normal

## Slide 98: Neighborhood Selection – KNN vs Radius
KNN is like asking your 30 closest friends.
Radius is like asking everyone within 1 meter of you.
Choosing the right method affects the quality of normals.
Method | Description | Best For
KNN | Use a fixed number of nearest neighbors (e.g., K = 30) | Uniform-density clouds
Radius | Use all neighbors within a fixed radius (e.g., R = 0.1 m) | Uneven or sparse clouds

## Slide 99: Visualizing Normals
Normals are shown as short arrows growing out from each point
Useful for:
Detecting noisy areas
Debugging surface direction
Preparing for mesh generation
Open3D Code:
Downsample point cloud before estimating/visualizing normals.
o3d.visualization.draw_geometries([pcd], point_show_normal=True)

## Slide 100: Centering and Normalizing Before Normals
Normalization = Centering + Scaling to unit size

## Slide 101: sequence of Normalizing :
Center the point cloud → Subtract the mean from all points to shift the cloud to (0, 0, 0)
Scale (Normalize) the point cloud → Find the maximum distance from the origin → Divide all points by that distance → So the farthest point is now exactly at distance = 1
Why is this done in order?
If you don’t center the cloud first, your max distance will be from the wrong "middle"
That will lead to incorrect normalization, where the cloud is shifted or stretched oddly

## Slide 102: Why is this Normalization done in order?
If you don’t center the cloud first, your max distance will be from the wrong "middle"
That will lead to incorrect normalization, where the cloud is shifted or stretched oddly
Overall:
To normalize a cloud, we first center it so it’s sitting on the origin. Then we scale it down so all the points fit neatly inside a small space — like a ball with radius 1.

## Slide 103
Point Cloud Transformations

## Slide 104: Overview
Transformations allow us to move, rotate, and scale point clouds in 3D space
These are essential for aligning, visualizing, and analyzing 3D data
Main types of transformations:
Translation
Rotation
Scaling
Full transformation using a 4×4 matrix

## Slide 105: Translation
Translation (Moving the Point Cloud)
Shifts the entire point cloud in space without changing shape or direction
Example:
Result: The whole cloud moves to a new position
pcd.translate((3, 0, 1)) # Move 3 units in X, 1 unit up (Z)

## Slide 106: Rotation
Rotation (Turning the Point Cloud)
Rotates the point cloud around X, Y, or Z axis
Example:
Result: The cloud turns 45° around the Z-axis
R = pcd.get_rotation_matrix_from_xyz((0, 0, np.pi / 4)) pcd.rotate(R, center=(0, 0, 0))

## Slide 107: Scaling
Scaling (Resizing the Point Cloud)
Changes the size of the point cloud without moving its center
Example:
Result: The cloud becomes smaller or larger, but keeps shape
pcd.scale(0.5, center=pcd.get_center()) # Shrinks to half size

## Slide 108: What is a 4×4 Transformation Matrix?
A 4×4 transformation matrix is a single matrix that can apply:
Rotation
Translation
Scaling to a point cloud — all at once.
Scaling we can consider as optional

## Slide 109: The Structure:
| R11 R12 R13 Tx | ← Rotation + Translation
| R21 R22 R23 Ty |
| R31 R32 R33 Tz |
| 0 0 0 1 | ← Padding row (required)
What It Does :
Rotates the point cloud (R part)
Translates it to a new position (T part)
Keeps it structured as a single command
Component | Meaning
R11 to R33 | Rotation matrix (3×3)
Tx, Ty, Tz | Translation vector (how much to move)
Bottom row | Used for math — keeps the format consistent in 3D space

## Slide 110: Apply a Transformation Matrix in Open3D
Python :
Applies rotation and translation together in one shot
T = np.eye(4) T[:3, :3] = pcd.get_rotation_matrix_from_xyz((0, 0, np.pi / 4)) # 45° rotation T[:3, 3] = [2, 0, 1] # Translate in X and Z pcd.transform(T)

## Slide 111: Matrix Composition (Multiple Transforms)
You can combine transforms by multiplying matrices:
Python :
Order matters — Rotation before Translation ≠ Translation before Rotation
T_final = T3 @ T2 @ T1 pcd.transform(T_final)

## Slide 112: Verify Changes in RViz
Save transformed cloud:
Publish in ROS:
Open RViz:
  Set Fixed Frame = map
  Add PointCloud2, select /cloud_pcd
  View the position, direction, and size
  We can see the cloud shifted, rotated, and resized in RViz’s 3D space.
o3d.io.write_point_cloud("transformed_sample.pcd", pcd)
rosrun pcl_ros pcd_to_pointcloud transformed_sample.pcd 1.0 _frame_id:=map

## Slide 113
Advanced Visualization and Annotation

## Slide 114: Advanced Visualization and Annotation
Goal: Enhance point cloud understanding by visually highlighting different elements
We’ll learn to:
Color clusters or classes
Add annotations (lines, boxes)
Export screenshots of our visualizations

## Slide 115: Color Coding Clusters or Classes
What It Is:
Assign different colors to different parts of a point cloud
Helps visually separate objects or categories
Why It’s Useful:
Makes clustering or segmentation results easy to see
Used in labeling cars, pedestrians, buildings, etc.
Hands-on:
import numpy as np import open3d as o3d colors = [[1, 0, 0], [0, 1, 0], [0, 0, 1]] # Red, Green, Blue for i, cluster in enumerate(clusters): # clusters = list of PointClouds cluster.paint_uniform_color(colors[i])

## Slide 116: Adding Annotations – Lines Between Points
What It Is:
Draws a line connecting two points (e.g., path, direction)
Why It’s Useful:
Show routes, measurements, object relationships
Hands-on:
from open3d.geometry import LineSet line = LineSet(points=..., lines=...)

## Slide 117
Bounding boxes help highlight and isolate objects in a point cloud (e.g., cars, people, surfaces)
They make objects easier to identify and analyze by visually separating them from the background

## Slide 118: Exporting Images or Screenshots
What It Is:
Save a screenshot of your visualized scene
Why It’s Useful:
Create reports, share results, or document output
Hands-on:
Use after coloring, boxing, or adding lines.
vis.capture_screen_image("output.png")

## Slide 119: Why It Matters
Feature | What It Does | Use Case
Color Coding | Visually separates groups or classes | Object segmentation
Boxes | Show where an object is in 3D space | Detection, object tracking
Lines | Connect important points | Paths, angles, relationships
Export | Capture the current view | Reports, sharing, debugging

## Slide 120
Segmentation Basics

## Slide 121: What is Segmentation?
Segmentation is the process of dividing a point cloud into separate, meaningful groups of points.
Helps identify individual objects or surfaces in a 3D scene.
It is a critical step before object detection, labeling, or tracking.
Example: In a point cloud of a street, segmentation helps split:
Points of cars
Points of pedestrians
Points of buildings or road

## Slide 122: Why Do We Need Segmentation?
Real-world point clouds are messy and unstructured.
Segmentation makes them easier to analyze and process.
Application | Benefit
Object Detection | Detect cars, humans, trees, etc.
Scene Understanding | Understand different parts of scene
Robot Navigation | Avoid obstacles, plan path

## Slide 123: Common Types of Segmentation
Type | Description | Example Use Case
Clustering | Groups points based on distance or density | Object separation
Plane Segmentation | Identifies flat surfaces (e.g., floor) | Ground or table detection
Region Growing | Expands based on smoothness/similarity | Wall or surface segmentation
Semantic Segmentation | Uses AI to assign class labels | Label road, car, person

## Slide 124: What is Clustering-Based Segmentation?
One of the simplest and most used segmentation methods
Groups points that are close together in space
Output: a set of clusters where each cluster = 1 object
Example: In a crowd scene, each person forms a cluster

## Slide 125: Clustering-Based Segmentation
The most common and simple form of segmentation
Clusters are formed based on distance between points
Common algorithms:
  DBSCAN
  Euclidean Clustering

## Slide 126: Introduction to DBSCAN Clustering
DBSCAN = Density-Based Spatial Clustering of Applications with Noise
It finds clusters based on how tightly packed the points are
Points too far from any group are treated as noise
It needs two parameters:
eps: Distance threshold to find neighbors
min_points: Minimum points required to form a cluster

## Slide 127: How DBSCAN Works
Pick a point
Look around within radius eps
If min_points neighbors found → form a cluster
Expand the cluster to include all reachable points
Points that don’t belong to any cluster → marked as noise

## Slide 128
Clustering and Labeling

## Slide 129: Objective
Goal :
Use DBSCAN to cluster a point cloud, color each cluster, and remove noise points.
We'll learn:
How to apply DBSCAN in code
How to visualize clusters with different colors
How to remove noise/outlier points

## Slide 130: Apply DBSCAN in Open3D
Python :
What Does This Code Do?
Applies DBSCAN clustering on the point cloud
Assigns a label to every point based on its cluster
How to Count Clusters:
total_clusters = labels.max() + 1
Add +1 because cluster IDs start from 0
labels = np.array(pcd.cluster_dbscan(eps=0.2, min_points=10, print_progress=True))
Label | Meaning
0 | Cluster 0 (first detected object)
1 | Cluster 1
2 | Cluster 2
... | More clusters
-1 | Noise point (does not belong to any group)

## Slide 131: Example:
1000 points in total
4 detected clusters → labels 0, 1, 2, 3
150 points labeled -1 → considered noise
Use these labels to:
Color each cluster differently
Remove noise points
Analyze individual objects in the scene

## Slide 132: How it looks ?

## Slide 133: Color Each Cluster Differently
Python
This makes each cluster visually distinct
Use this for visualization in RViz or Open3D
import matplotlib.pyplot as plt max_label = labels.max() colors = plt.get_cmap("tab20")(labels / (max_label + 1)) colors[labels < 0] = [0, 0, 0] # Color noise as black pcd.colors = o3d.utility.Vector3dVector(colors[:, :3])

## Slide 134: Remove Noise Points
To keep only valid clusters (no noise):
This filters out all points labeled -1 (noise)
Keeps only clustered objects
clean_indices = np.where(labels >= 0)[0] pcd_clean = pcd.select_by_index(clean_indices)

## Slide 135: Summary
Step | What It Does
Apply DBSCAN | Group nearby points into clusters
Color by Label | Assign unique color to each group
Remove Noise (opt.) | Delete scattered, irrelevant points

## Slide 136
Bounding Boxes & Geometric Calculations

## Slide 137: Bounding Boxes & Geometric Calculations
Topics Covered:
AABB (Axis-Aligned Bounding Box)
OBB (Oriented Bounding Box)
Centroid and volume calculations

## Slide 138: cloud of points in 3D
Imagine you have a cloud of points in 3D — like dots floating in space, forming the shape of an object (e.g., a chair, box, or rock).
Then :
How do we measure that shape?
How do we describe its size, position, or orientation?
How do we wrap it in something simple to work with?
Bounding boxes and centroid help us do exactly that.

## Slide 139: What are Bounding Boxes?
Bounding boxes (AABB & OBB) help us wrap complex point cloud shapes inside simple boxes to make processing and understanding easier.
Purpose of Bounding Boxes ?
Simplify complex 3D objects
Estimate size, position, and center
Speed up calculations
Used in object detection, tracking, and grasping

## Slide 140: How it looks ?

## Slide 141: AABB – Axis-Aligned Bounding Box
What is AABB?
AABB is a box that tightly fits around the object
Its edges are always aligned with X, Y, Z axes
So it’s like a box standing straight — no rotation
Why use it?
It’s very fast to calculate
Useful when we want a quick estimate of where an object is
Easy to use in filtering, cropping, collision detection
aabb = pcd.get_axis_aligned_bounding_box() aabb.color = (1, 0, 0) # Red Volume of the AABB: aabb_extent = aabb.get_extent() # [Length, Width, Height] volume_aabb = np.prod(aabb_extent) print("AABB Volume:", volume_aabb)

## Slide 142: OBB – Oriented Bounding Box ?
What is OBB?
OBB is also a box, but it can rotate
It fits the object more tightly, even if it’s diagonal or tilted
It’s like wrapping the object with a box that turns with it
Why use it?
More accurate than AABB
Used in robotics for things like grasping or packaging
Helpful when objects are not axis-aligned
obb = pcd.get_oriented_bounding_box() obb.color = (0, 1, 0) # Green Volume of the OBB: obb_extent = obb.extent volume_obb = np.prod(obb_extent) print("OBB Volume:", volume_obb)

## Slide 143: What is Centroid?
What is Centroid?
The centroid is the average of all point positions
Think of it as the balance point of the shape
Why use it?
Helps us know where the center of the object is
Useful for placing labels, or anchoring something
centroid = np.mean(np.asarray(pcd.points), axis=0) print("Centroid:", centroid)

## Slide 144: Visualize Everything Together ?
What we see when we visualize:
The original point cloud shape
A red box around it (AABB)
A green, tilted box (OBB)
We know the center (centroid) and volume of each box
Visualization : o3d.visualization.draw_geometries([pcd, aabb, obb])

## Slide 145: Real-Life Analogy
Concept | Real-Life Analogy
AABB | A straight box placed flat on a table
OBB | A tilted box that hugs the object perfectly
Centroid | Balance point of the object
Volume | How much water the box could hold

## Slide 146: Key Takeaways
AABB: Fast and simple for filtering
OBB: Precise, handles rotation, great for robotics
Centroid: Finds object center
Volume: Helps filter or sort objects

## Slide 147
Distance Measures & Metrics

## Slide 148: Objectives :
Euclidean distance between clouds/points
Distance to planes (e.g., ground plane)

## Slide 149: Euclidean Distance Between Points
It's the straight-line distance between two points in space.
Like using a scale to measure from one point to another — the shortest possible path.
Example: If we have p1 = [1, 2, 3]
p2 = [4, 5, 6]
Then:
This line:
Subtracts the two points: [4-1, 5-2, 6-3] = [3, 3, 3]
Computes the length of the resulting vector, which is the distance.
distance = np.linalg.norm(np.array(p1) - np.array(p2))

## Slide 150: Distance Between Two Point Clouds ?
You want to know how far each point in one cloud is from the nearest point in another cloud.
How do we do that?
For each point in Cloud A, find the nearest point in Cloud B using KDTree
Then compute Euclidean distance between them
Helps compare similarity or alignment of two clouds
Sample Code:
pcd_tree = o3d.geometry.KDTreeFlann(pcd2) for point in pcd1.points: [_, _, dists] = pcd_tree.search_knn_vector_3d(point, 1)

## Slide 151: KDTree – Fast Nearest Neighbor Search
KDTree is a data structure that allows fast search of nearby points
Especially useful when working with large point clouds
Used with Euclidean distance to find closest points efficiently
KDTree is helpful for ?
Comparing how two shapes differ
Checking alignment errors
Change detection in point clouds

## Slide 152: Distance to a Plane ?
Why measure distance to a plane?
To know how high a point/object is from the ground or some flat surface
First: Detect the Plane :
This uses RANSAC to find the best flat surface in your cloud (like the floor or a table).
You get values: a, b, c, d
That define the plane equation: Ax + By + Cz + D = 0
plane_model, inliers = pcd.segment_plane(...)

## Slide 153: Plane Fitting using RANSAC (Open3D)
Then:
Measure distance of any point to the plane
Code example :
RANSAC is used to fit a plane even when there are noisy points
Randomly picks points, fits many planes, and keeps the best one
Helps find clean ground surfaces in real-world clouds
distance = ¦Ax + By + Cz + D¦ / sqrt(A^2 + B^2 + C^2)
plane_model, inliers = pcd.segment_plane( distance_threshold=0.01, ransac_n=3, num_iterations=1000 )

## Slide 154: Distance Measures & Metrics – Visual
Euclidean Distance ⟶ Straight-line distance between two 3D points
KDTree ⟶ Quickly finds nearest neighbors using spatial indexing
Distance to Plane ⟶ Measures point height from a flat surface (like ground)
RANSAC ⟶ Fits the best plane by ignoring noisy/outlier points

## Slide 155
Data Preparation for Deep Learning

## Slide 156: Objectives :
Normalize and scale data
Downsample to fixed point counts (e.g., 1024)
Format conversion (.pcd → .npy)

## Slide 157: Normalize and Scale Point Cloud
Centering: Shift the cloud so its centroid is at the origin
Scaling: Scale all points to fit inside a unit sphere (radius = 1)y
Helps deep learning models learn better by removing scale/position bias
center = np.mean(points, axis=0) points -= center
max_dist = np.max(np.linalg.norm(points, axis=1)) points /= max_dist

## Slide 158: Downsample to Fixed Number of Points (e.g., 1024)
Deep learning models (like PointNet) need fixed-size inputs
1024 is commonly used because:
It balances detail and speed
Matches research standards (e.g., PointNet)
Sampling:
if len(points) >= 1024: indices = np.random.choice(len(points), 1024, replace=False) else: indices = np.random.choice(len(points), 1024, replace=True) sampled = points[indices]

## Slide 159: Format Conversion: .pcd → .npy
.npy is a fast, compact format used in deep learning libraries
Easily saves and loads point cloud arrays
To Save:
To Load Later:
np.save("cloud_sample.npy", sampled)
data = np.load("cloud_sample.npy")

## Slide 160: How it looks ?
start by centering and scaling the point cloud (normalize it).
Then we reduce the number of points (downsample to 1024).
Finally, we save it in .npy format so it’s ready for deep learning.”

## Slide 161: Key Steps
Step | Purpose
Normalize + Scale | Center cloud, remove size/position bias
Downsample to 1024 | Ensure fixed input size for model
Save as .npy | Efficient data storage for training

## Slide 162: Thank You